DATA STREAM A240  SPECIFICATION

..PAGE

SPECIFICATIONS FOR DATA STREAM INFORMATION TEVES ABS/ASR

--------------------------------------------------------

ABS/ASR USAGE:

1994    2,3,4H 3,4C

1995    3,4G

*                    1995    2,3,4H 3,4C

DATA PIN  : READ DATA ON PIN "M" OF ALDL CONNECTOR

DATA PIN  : READ DATA ON PIN "9" OF 16 PIN ALDL CONNECTOR

BAUD RATE : 8192 BAUD - BI-DIRECTIONAL

..PAGE

MODE 0 (RETURN TO NORMAL MODE)

ALDL REQUEST:

- MESSAGE ID     = $F9

- MESSAGE LENGTH = $56

- MODE           = $00

- SUM CHECK      = $B1

MODE 1 (TRANSMIT ALDL DATA LIST)

ALDL REQUEST:

- MESSAGE ID     = $F9

- MESSAGE LENGTH = $57

- MODE           = $01

- MESSAGE        = $00

- SUM CHECK      = $AF

THE ABS/ASR CONTROLLER WILL RESPOND WITH THE FOLLOWING MESSAGE:

- MESSAGE ID     = $F9

- MESSAGE LENGTH = $5D

- MODE           = $01

- DATA BYTE 1

.

.

- DATA BYTE 7

- SUM CHECK

MODE 10 (CLEAR MALFUNCTION CODES)

ALDL REQUEST:

- MESSAGE ID     = $F9

- MESSAGE LENGTH = $56

- MODE           = $0A

- SUM CHECK      = $A7

THE ABS/TCS WILL RESPOND WITH THE FOLLOWING MESSAGE:

- MESSAGE ID     = $F9

- MESSAGE LENGTH = $56

- MODE           = $0A

- SUM CHECK      = $A7

NORMAL MODE MESSAGE (PCM TO ABS OR ABS/TBS)

- MESSAGE ID     = $90

- MESSAGE LENGTH = $59

- DATA BYTE 1

.

.

- DATA BYTE 4

- SUM CHECK

NORMAL MODE MESSAGE (ABS/TCS TO PCM)

- MESSAGE ID     = $91

- MESSAGE LENGTH = $59

- DATA BYTE 1

.

.

- DATA BYTE 4

- SUM CHECK

..PAGE

..HEAD02L ALDL DATA LIST

..HEAD03L NUMBER OF DATA WORDS - 7

..HEAD04L ALDL MODE 1 DATA LIST

WORD #   DATA NAME    DESCRIPTION

1      PROGRAM ID (SERVICE PROTOCOL)

2      PROGRAM ID (SOFTWARE VERSION)

NOTE: IN ALL CASES A VALUE OF 0 EQUALS "CODE NOT SET" AND 1 EQUALS "CODE SET".

3      MALFUNCTION CODE FLAG #1

7       CODE 21 - FRONT RIGHT SENSOR CIRCUIT OPEN/SHORTED

6       CODE 22 - INTERMITTENT SIGNAL, FRONT RIGHT SENSOR

5       CODE 23 - MISSING SIGNAL, FRONT RIGHT SENSOR

4       NOT USED

3       CODE 25 - FRONT LEFT SENSOR CIRCUIT OPEN/SHORTED

2       CODE 26 - INTERMITTENT SIGNAL, FRONT LEFT SENSOR

1       CODE 27 - MISSING SIGNAL, FRONT LEFT SENSOR

0       NOT USED

4      MALFUNCTION CODE FLAG #2

7       CODE 31 - REAR RIGHT SENSOR CIRCUIT OPEN/SHORTED

6       CODE 32 - INTERMITTENT SIGNAL, RIGHT REAR SENSOR

5       CODE 33 - MISSING SIGNAL, REAR RIGHT SENSOR

4       NOT USED

3       CODE 35 - REAR LEFT SENSOR CIRCUIT OPEN/SHORTED

2       CODE 36 - INTERMITTENT SIGNAL, REAR LEFT SENSOR

1       CODE 37 - MISSING SIGNAL, REAR LEFT SENSOR

0       NOT USED

5      MALFUNCTION CODE FLAG #3

7       CODE 41 - ELECTRICAL DISTURBANCE INLET VALVE

(CIRCUIT - FRONT RIGHT)

6       CODE 42 - ELECTRICAL DISTURBANCE OUTLET VALVE

(CIRCUIT - FRONT RIGHT)

5       CODE 44 - ELECTRICAL DISTURBANCE ISOLATION VALVE SV1

(CIRCUIT - FRONT LEFT)

NOTE: TCS ONLY

4       NOT USED

3       CODE 45 - ELECTRICAL DISTURBANCE INLET VALVE

(CIRCUIT - FRONT LEFT)

2       CODE 46 - ELECTRICAL DISTURBANCE OUTLET VALVE

(CIRCUIT - FRONT LEFT)

1       CODE 48 - ELECTRICAL DISTURBANCE ISOLATION VALVE SV2

(CIRCUIT -FRONT RIGHT)

NOTE: TCS ONLY

0        NOT USED

6      MALFUNCTION CODE FLAG #4

7       CODE 51 - ELECTRICAL DISTURBANCE INLET VALVE

(CIRCUIT - REAR RIGHT)

6       CODE 52 - ELECTRICAL DISTURBANCE OUTLET VALVE

(CIRCUIT - REAR RIGHT)

5       CODE 76 - UART SDL CIRCUIT/SIGNAL

4       NOT USED

3       CODE 55 - ELECTRICAL DISTURBANCE INLET VALVE

(CIRCUIT - REAR LEFT)

2       CODE 56 - ELECTRICAL DISTURBANCE OUTLET VALVE

(CIRCUIT - REAR LEFT)

1       CODE 77 - DELIVERED TORQUE PWM CIRCUIT/SIGNAL

NOTE: TCS ONLY

0       NOT USED

7      MALFUNCTION CODE FLAG #5

7       NOT USED

6       CODE 75 - PCM REQUESTED TCS DISABLE

NOTE: TCS ONLY

5       CODE 74 - PMV PRESSURE SWITCH CIRCUIT

NOTE: TCS ONLY

4       CODE 62 - PUMP PRESSURE FAULT DURING ABS STOP

3       CODE 61 - PUMP MOTOR RUN FAULT

2       CODE 71 - CHECKSUM ERROR

1       CODE 72 - TRAVEL SWITCH INPUT NOT PROCESSABLE

0       CODE 73 - FLUID LEVEL SWITCH INPUT NOT PROCESSABLE

..HEAD02L NORMAL MODE MESSAGE $90

..HEAD03L NUMBER OF DATA WORDS - 4

..HEAD04L PCM TO ABS OR ABS/TCS

WORD #   DATA NAME    DESCRIPTION

1      ENGINE RPM

RESOLUTION: 25 RPM/BIT

RANGE: 0 TO 6375 RPM

2      ENGINE IDENTIFIER FOR TCS CALIBRATION

3.8L EV6 = $01

3.8L SC = $02

4.0L NORTHSTAR = $03

3.8L ERV6 = $04 (1995 APPLICATION)

3.8L ERV6 SC = $05 (PENDING 1996 APPLICATION)

3      DELIVERED ENGINE TORQUE VALUE

RESOLUTION:.392% (100%/255) PER BIT

RANGE: 0 TO 100% TORQUE

4      STATUS BITS

7       1 = TCS ALLOWED

6       1 = TCS NOT FAILED

5       1 = TCS ACTIVE

4-2     TRANSMISSION GEAR

CODE   DESCRIPTION

----   -----------

000   REVERSE

001   FIRST

010   SECOND

011   THIRD

100   FOURTH

101   N/A (FIFTH)

110   N/A (SIXTH)

111   PARK/NEUTRAL

1       1 = TCC LOCKED

0       NOT USED

..HEAD02L NORMAL MODE MESSAGE $91

..HEAD03L NUMBER OF DATA WORDS - 4

..HEAD04L ABS/TCS TO PCM

WORD #   DATA NAME    DESCRIPTION

1      VEHICLE SPEED AS COMPUTED BY TCS

RESOLUTION:1 KPH

RANGE: 0 TO 255 KPH

2      STATUS BITS

7       1 = BRAKE LIGHTS ON, SWITCH CLOSED

6       1 = PEDAL TRAVEL SW OPEN

5       1 = ABS ACTIVE

4       1 = ABS INHIBITED

3       1 = TCS EQUIPPED (IPC EAVESDROP)

2       NOT USED

1       NOT USED

0       NOT USED

3      REQUESTED ENGINE TORQUE VALUE

RESOLUTION: .392% (100%/255) PER BIT

RANGE: 0 TO 100% TORQUE

4      STATUS BITS

7       1 = TCS FAILED

6       1 = TCS ACTIVE (IPC EAVESDROP)

5       1 = LT RR WHEEL SPEED SENSOR NOT FAILED

4       1 = RT RR WHEEL SPEED SENSOR NOT FAILED

3       1 = TCS ALLOWED

2       1 = ILLUMINATE "TCS OFF" TELLTALE (IPC EAVESDROP)

1       NOT USED

0       NOT USED